## Slide 1
ANSYS Load Reconstruction Toolchain
Methodology & Theory — recovering applied loads from strain-gauge data
scripts/ansys_load_reconstruction · strain-gauge force identification by FE unit-load superposition

## Slide 2
The problem: from strains to loads
▸ Goal: estimate the applied loads L that a part experienced, from strains S measured by a gauge network
  – Forward map L → S is a cheap FE calculation
  – Inverse map S → L is the hard, error-sensitive direction (force identification / inverse problem)
▸ Why it matters for turbine structures:
  – recover in-service / test mission loads from instrumented hardware
  – cross-check applied test loads; monitor load paths
  – feed measured loads into downstream stress & life assessment
▸ The toolchain builds the forward model once, then inverts it per measured strain record
ANSYS Load Reconstruction Toolchain — Methodology & Theory
1

## Slide 3
Forward model & assumptions
▸ Linear elastic superposition is the foundation:
  – strain at channel i is a linear combination of the applied loads
    εᵢ = Σⱼ Aᵢⱼ Lⱼ ⇔ S = A·L
▸ Valid when:
  – material behaviour is linear elastic
  – deformations small (linear strain–displacement)
  – contacts, supports, preload, load paths are load-independent
  – the real loading lies in the span of the unit-load basis
▸ If violated, least squares still returns numbers — but not physically meaningful loads
ANSYS Load Reconstruction Toolchain — Methodology & Theory
2

## Slide 4
Workflow at a glance
Four production scripts (build A → export local strains → placement gradients → invert) plus two inspection helpers.
Execution pattern: Mechanical runs each button in IronPython (no NumPy), which writes a CPython worker and launches external python.exe for the array math.
ANSYS Load Reconstruction Toolchain — Methodology & Theory
3

## Slide 5
Mechanical model contract
▸ Naming conventions the scripts rely on:
  – Unit_Load_Study_LC_* — one analysis per unit load case (tree order = column order of A)
  – StrainX_SG* — Normal Elastic Strain results, one per channel
  – SG_Grid_Body_* — finite shell body modelling each gauge footprint
  – CS_SG_Ch_* — per-gauge local coordinate system (measurement axis)
  – NS_of_faces_of_SG_test_parts — instrumented surface
▸ Scoping & averaging:
  – each StrainX_SG* scoped to its SG_Grid_Body* → .Average.Value is the finite-grid mean
  – channel order identical across all analyses and the measured-strain file
    do NOT double-average; do NOT use equivalent stress/strain for placement
ANSYS Load Reconstruction Toolchain — Methodology & Theory
4

## Slide 6
Theory — the strain sensitivity matrix A
▸ Aᵢⱼ = ∂εᵢ/∂Fⱼ : strain at channel i per unit of load j
  – column j = the gauge response to unit load case j
  – rows = channels, columns = load components
  – benchmark shape: 42 × 3
▸ Built from unit-load FE studies, preload-subtracted
  – isolates the incremental response to each unit load
▸ Near-collinear columns (similar gauge response) →
  – small singular value → high condition number
ANSYS Load Reconstruction Toolchain — Methodology & Theory
5

## Slide 7
Tool 1 — sensitivity matrix generator
    get_strain_sensitivity_matrix_from_unit_load_cases_in_mechanical_v0.py
▸ Runs in Mechanical (IronPython) + spawned CPython
  – Scans Unit_Load_Study_LC_* analyses in tree order
  – Reads each StrainX_SG* .Average.Value at the unit-load step minus the preload step
  – Preload subtraction → each column is the pure incremental unit-load response
▸ Outputs:
  – strain_sensitivity_matrix.csv (the matrix A)
  – strain_sensitivity_metadata.json (rank, singular values, condition number, scope evidence)
  – strain_sensitivity_placement_sensitivity.csv (template, filled by Tool 3)
    CPython worker adds the SVD diagnostics
ANSYS Load Reconstruction Toolchain — Methodology & Theory
6

## Slide 8
Theory — least squares via SVD (not normal equations)
▸ Per time point, solve the overdetermined system:
  – implemented as np.linalg.lstsq(A, S.T, rcond=None) — a direct SVD
▸ Why not the normal equations?
  – forming AᵀA squares the condition number
  – inv() is unstable for ill-conditioned / rank-deficient A
  – SVD truncates negligible singular values → graceful rank handling
▸ Error inputs never change the point estimate — only the uncertainty bands
ANSYS Load Reconstruction Toolchain — Methodology & Theory
7

## Slide 9
Theory — conditioning & error amplification
▸ Condition number from the singular spectrum:
  – benchmark A: κ ≈ 1.11 × 10⁵
▸ Large κ ⇒ small strain error → large load error
  – the load component aligned with σ_min is weakly observed
  – inverting a 'flat' response ellipse magnifies noise
▸ Baseline stays plain least squares; add regularization only if validation demands it
ANSYS Load Reconstruction Toolchain — Methodology & Theory
8

## Slide 10
Tool 4 — load reconstruction solver
    load_reconstruction_function_with_errors_weighting_function_v1.py
▸ Inputs: SG_FEA_strain_data.csv (measured) + strain_sensitivity_matrix.csv (A)
  – SVD least-squares point estimate per time point
  – residual RMS, rank, singular values, κ recorded
▸ Outputs:
  – estimated_loads_with_errors_per_gauge_RMS.csv (point estimate)
  – estimated_loads_uncertainty.csv (Mean / Std / P2.5 / P97.5)
  – load_reconstruction_diagnostics.json (check this first)
  – load_reconstruction_validation.csv (if known_loads.csv supplied)
ANSYS Load Reconstruction Toolchain — Methodology & Theory
9

## Slide 11
Theory — local strain measurement
▸ A gauge reads the normal strain along its own axis n:
  – εₙ = nᵀ ε n (tensor contraction)
  – per-channel local CS defines the measurement direction
▸ Same strain state reads differently per orientation
  – 0° / 45° / 90° → 100 / 65 / −30 µε (example)
▸ This projection is local_x_normal_strain() in the exporter
ANSYS Load Reconstruction Toolchain — Methodology & Theory
10

## Slide 12
Tool 2 — DPF local strain + geometry exporter
    get_local_strains_and_SG_geo_data_around_each_SG_grid_dpf.py (preferred)
▸ Exports, per gauge channel:
  – local strain cloud within a radius (StrainX_around_*.csv)
  – local coordinate systems (SG_coordinate_matrix.csv)
  – SG_Grid_Body_* vertices, global and in local frame
▸ DPF reads the .rst directly — no temporary tree objects
  – midside (parabolic) nodes filled via extend_to_mid_nodes_fc
  – batch via SG_LOCAL_DPF_* env vars; writes diagnostics JSON
    Legacy contour exporter (...grid.py) kept for Mechanical-native inspection
ANSYS Load Reconstruction Toolchain — Methodology & Theory
11

## Slide 13
Theory — placement sensitivity
▸ A finite-size gauge can only be bonded to finite accuracy
  – shifting the footprint changes the averaged strain
  – Δε ≈ (∂ε/∂x)·dx + (∂ε/∂y)·dy
▸ Compute the spatial gradient of the footprint-averaged strain:
  – interpolate the cloud (scipy.griddata, linear + nearest fill)
  – rigidly shift the footprint ±h and central-difference the mean
    h = 0.1 mm is a derivative step, not the placement uncertainty
ANSYS Load Reconstruction Toolchain — Methodology & Theory
12

## Slide 14
Tool 3 — placement sensitivity calculator
    calculate_placement_sensitivity_from_local_strains.py
▸ IronPython button + spawned CPython worker (NumPy/SciPy)
  – Rotates each exported cloud into its CS_SG_Ch_* frame
  – Interpolates strain onto the footprint grid; shifts ±h in local x, y
  – Central-differences the footprint-averaged strain
▸ Output: strain_sensitivity_placement_sensitivity.csv
  – d_epsilon_d_x_per_mm, d_epsilon_d_y_per_mm, gradient_norm_per_mm
  – per (channel, load case); feeds the positioning term of Tool 4
    Least-squares-plane fallback if SciPy interpolation is unavailable
ANSYS Load Reconstruction Toolchain — Methodology & Theory
13

## Slide 15
Theory — uncertainty propagation (Monte Carlo)
▸ Point estimate is pure least squares; errors drive the bands only
▸ Three error sources, perturb measured strain & re-solve (1000×):
  – additive signal noise: ε* = ε + N(0, σ²) per (time, channel)
  – gage factor: ε* = ε·(1+N(0,σ²)) systematic per channel, held over time
  – positioning: Δε = ∂ε/∂x·dx + ∂ε/∂y·dy, gradient-driven
▸ Positioning gradient is load-weighted: dstrain_dx = L_hat @ gx.T
  – → position error scales with how hard the part is driven
▸ Reported per load: Mean, Std, P2.5, P97.5
ANSYS Load Reconstruction Toolchain — Methodology & Theory
14

## Slide 16
Theory — thermal / apparent strain (the silent trap)
▸ The solver only knows S = A·L
  – a load-independent thermal/apparent strain present in S …
  – … is projected onto the load basis and reported as FAKE load
▸ Mitigation:
  – supply SG_thermal_apparent_strain_data.csv (subtracted before solving)
  – diagnostics warn if Isothermal Heating exists and no file is given
    Always relevant for thermally-loaded turbine hardware
ANSYS Load Reconstruction Toolchain — Methodology & Theory
15

## Slide 17
Helper — position error contour (inspection only)
    get_position_error_contour_v0.3.py
▸ For each reference gauge (CS_SG_Ch_*_2):
  – find the nearest mesh node to the reference position
  – map the field difference to neighbours within a user radius
▸ Outputs SG_positioning_errors.csv + an in-Mechanical CSV-Plot contour
  – Use it to visualise where placement error hurts most
▸ NOT the source of reconstruction placement sensitivity
  – it does not shift each finite footprint in the channel's local frame — that is Tool 3
ANSYS Load Reconstruction Toolchain — Methodology & Theory
16

## Slide 18
Benchmark evidence
    Benchmark project: load_reconstruction_v0.wbpj, system 'Arbitrary Loads with Isothermal Heating'
▸ Model:
  – 42 SG_Grid_Body_* shell/sheet bodies (CAERep: GeometryType=Sheet, ModelType=Shell)
  – gauge grid bounding-box diagonal ≈ 4.7 mm
▸ Sensitivity matrix:
  – A is 42 × 3, full rank 3
  – condition number κ ≈ 1.11 × 10⁵
▸ Solver:
  – upgraded SVD OLS point estimate matches the legacy output to roundoff
ANSYS Load Reconstruction Toolchain — Methodology & Theory
17

## Slide 19
Diagnostics & trust checklist
▸ Check load_reconstruction_diagnostics.json first. Before trusting loads:
  – diagnostics JSON exists; normal_equations_used = false
  – rank equals the number of load columns
  – condition_number is acceptable for the application
  – metadata_confirms_shell_channel_average = true (when metadata present)
  – no channel-order warning
  – thermal compensation supplied if thermal loading exists
  – placement derivatives are numeric (not 'not_computed') if positioning matters
  – known_loads.csv validation error acceptable, where available
ANSYS Load Reconstruction Toolchain — Methodology & Theory
18

## Slide 20
Limitations
▸ The method does NOT automatically handle:
  – nonlinear material, geometry, or contact behaviour (breaks S = A·L)
  – loading outside the span of the unit-load basis
  – FE model error baked into A
  – transverse-sensitivity correction of the gauges
  – physical calibration against known loads
  – regularization-parameter selection
  – missing or incorrect gauge scoping
▸ Treat reconstructed loads as engineering estimates — validate whenever possible
ANSYS Load Reconstruction Toolchain — Methodology & Theory
19

## Slide 21
Summary — key takeaways
S = A·L solved by SVD least squares is a clean, defensible baseline estimator.
Build A once from preload-subtracted unit-load FE studies; .Average.Value gives finite-grid strain.
Accuracy is governed by basis span, conditioning of A (benchmark κ ≈ 1.1×10⁵), and honest error accounting.
Uncertainty = Monte Carlo over signal noise, gage factor, and gradient-driven positioning — never the point estimate.
Thermal/apparent strain must be compensated or it reconstructs as fake load.
DPF extraction is the preferred (fast, batch) path; the IronPython→CPython pattern runs the heavy math.
Always check load_reconstruction_diagnostics.json and validate against known loads when you can.
Companion notebook: load_reconstruction_methodology_walkthrough.ipynb · Guide: LOAD_RECONSTRUCTION_USER_GUIDE.md